## Slide 1: PANDAA Localization Using Ambient Sound
Team Google

## Slide 2: Team Google
Client
  Trevor Pering, contact (grafnu@gmail.com)
  Pei Zhang, advisor (peizhang@cmu.edu)
Team
  Dilip Gudlur (dgudlur@cmu.edu)
  Divya Vavili (divya.vavili@west.cmu.edu)
  Fabian Popa (fabian.popa@west.cmu.edu)
  Qi Zheng (qi.zheng@west.cmu.edu)

## Slide 3: Agenda
Project Overview
Related Work
Project Architecture
Implementation
Measuring Outcome
Project Management
Demo

## Slide 4: Project Overview
PANDAA - novel localization technique that uses ambient sounds to localize a network of static sensors
PANDAA isolates mixed ambient sounds that already exist in the environment (claps, speech, cough, walking sounds, etc.) to localize the devices

## Slide 5: Technical Problem
How to determine the relative physical arrangements of networked devices?
Requirements
  Accurate (sub-meter)
  Work on off-the-self devices, minimal requirement of specialized hardware
  Non-intrusive, automated operation and maintenance

## Slide 6: Related Work (Indoor Localization)
 | Desired Accuracy | No Specialized Hardware | Non-intrusiveness
WiFi signal strength range/fingerprint | X | ✓ | ✓
Ultrasound-RF (Cricket) | ✓ | X | ✓
Audible chirp ranging (BeepBeep) | ✓ | ✓ | X
Ambient sound ranging (PANDAA) | ✓ | ✓ | ✓
Borrowed from Zheng's slides under his acknowledgement
Notes:     add one more column - autonomous setup

## Slide 7: PANDAA (in simple terms)
(0, 0)
(x1, y1)
(x2, y2)
(x3, y3)
(x4, y4)
(x5, y5)
Borrowed from Zheng's slides under his acknowledgement

## Slide 8: Project Architecture
1. Pre-processing
3. Arrangement Detection
2. Pairwise Distance Estimation
Ambient Sound (Input)
Microphone
Framing
Impulsive Sound Extraction
reduce 80%~99.9% raw data
Two-tier TDoA Aggregation
Compensation of Pairwise TDoA Errors
Arrangement Detection
TDoA Estimation
Relative Device Locations (Output)
Borrowed from Zheng's slides under his acknowledgement
Notes: arrows
lines
mention some will not be addressed
mention Two-tier will handle ambient noise

## Slide 9: Implementation

## Slide 10: Demonstration Setup

## Slide 11: Raw Audio Synchronization
Unsynchronized audio from devices
Audio after synchronization

## Slide 12: Raw Audio Synchronization
Audio after synchronization
(Magnified view)

## Slide 13: Peak Detection
What is peak?
  Audio -> frames
    100ms, 22,050Hz -> 2205 samples in one frame
  Rules
    Detect impulsive sounds: short duration + higher amplitude (e.g. claps)
    One frame contains at most one clap
    The first peak represents the clap

## Slide 14: Peak Detection
A

## Slide 15: Implementation
RMS: Root Mean Square
  The power of the sound
  Slow-window RMS
    1000 samples
    Noise floor
  Fast-window RMS
    50 samples
    Appearance of a peak

## Slide 16: Implementation
Fast-window RMS
Slow-window RMS

## Slide 17: Results
Quiet Ambient Noisy Ambient Normal Ambient

## Slide 18: TDOA (Time Difference of Arrival)
Objective: match impulses in two synchronized intervals
Frame 1
Frame 2

## Slide 19: TDOA (Time Difference of Arrival)
Algorithm: look at all plausible pairs of impulses
Frame 1
Frame 2
d

## Slide 20: TDOA (Time Difference of Arrival)
Algorithm: get the closest pairs time-wise
Frame 1
Frame 2
d

## Slide 21: TDOA (Time Difference of Arrival)
Algorithm: remember pair and distance, then advance
Frame 1
Frame 2
d

## Slide 22: TDOA (Time Difference of Arrival)
Algorithm: remember pair and distance, then advance
Frame 1
Frame 2
d

## Slide 23: TDOA (Time Difference of Arrival)
Algorithm: remember pair and distance, then advance
Frame 1
Frame 2
d

## Slide 24: TDOA (Time Difference of Arrival)
Algorithm: remember pair and distance, then advance
Frame 1
Frame 2
d

## Slide 25: TDOA (Time Difference of Arrival)
Algorithm: sort potential matches by distance
Frame 1
Frame 2
2
1
3
4

## Slide 26: TDOA (Time Difference of Arrival)
Algorithm: accept in decreasing order of distance
Frame 1
Frame 2
2
1
3
4

## Slide 27: TDOA (Time Difference of Arrival)
Algorithm: every impulse can only be matched once
Frame 1
Frame 2
2
1
3
4

## Slide 28: TDOA (Time Difference of Arrival)
Algorithm: final list of matches is a subset
Frame 1
Frame 2

## Slide 29: Arrangement Detection
Geometry Detection
  pairwise distances “comprehensive” distance matrix
  distance matrix coordinate matrix (using MDS)
MDS (Multi Dimensional Scaling) – key component
  similarity of data objects geometric positions
  Java library for MDS

## Slide 30
Device | A | B | C | D | E
A | 0 | 0 | 10 | 10 | 5
B | 0 | 0 | 10 | 10 | 5
C | -10 | -10 | 0 | 0 | -5
D | -10 | -10 | 0 | 0 | -5
E | -5 | -5 | 5 | 5 | 0
X | Y
5.16263035 | 2.97380274
4.95503652 | 3.95185523
-5.03470857 | 2.84630802
-5.24230241 | 3.8243605
-0.55882061 | 5.84421285
MDS in Action
Pairwise Distances
Coordinate Matrix
Geometry of Devices

## Slide 31: Measuring Outcome
Root Mean Square for an estimate of error
  Variation of the actual and estimated locations of the vertices
  Observation1: Single sound source nearer to the devices
  produce better impulses and thereby better localization
  Observation2: RMS error varies with the number of impulses processed
  Observation3: Triangle of devices with music as sound source produces 600mm error when 15 impulses are processed and reduces to 300 mm when 35 impulses are processed.

## Slide 32: Project Management
Weekly meetings with Client every Friday via video chat
Face to face meetings to resolve complex issues
Google applications (Hangout and Docs) used
  efficiently for task management and meetings
Extensive use of Github for maintenance of code repository
Maintenance of Engineering Notebook to track our progress/failures

## Slide 33: Project Management
Task identification and division among the four team members
High involvement of client in architecture design and implementation details
Client addressed individual team member queries via email threads
Extensive code reviews to identify issues at the early stages
Emphasis on correct and good quality of source code

## Slide 34: Acknowledgements
Dr. Trevor Pering – For such a good learning experience
Dr. Pei Zhang – For guidance throughout the project
Zheng Sun – For technical expertise in the project

## Slide 35: Thanks!!
Open to Questions…
And demo time…. See it in Action